## Slide 1
UNZ 261/017
13118
IAF
UNZ 286/008
8336
FAF
UNZ 015/008
3076
Approach NW Field – RWY 06R: Commence approach at the UNZ261017 at 13118 ft, heading 062 degrees. Descend to the Initial Approach Fix, UNZ286008 at 8336 ft. Maintaining 062 heading to the Final Approach Fix, the UNZ015008 at 3076 ft, continue approach to landing

## Slide 2
UAM 051/023
13126
IAF
UAM 044/013
8344
FAF
UAM 353/004
3084
Approach NW Field – RWY 24L: Commence approach at the UAM051023 at 13126 ft, heading 242 degrees. Descend to the Initial Approach Fix, UAM044013 at 8334 ft. Maintaining 242 heading to the Final Approach Fix, the UAM353004 at 3084, continue approach to landing.

## Slide 3
UAM 309/005
8000
UAM 314/007
8000
UAM 290/009
8000
UNZ 357/009
8000
IAF
UNZ 335/009
6289
UNZ 337/007
5732
UNZ 341/006
5114
UNZ 009/007
3554
FAF
UAM 015/008
3076
Missed Approach (C4) NW Field – RWY 06R: Commence missed approach at the UAM292005. At 8000 ft, heading 048 degrees. Turn left heading 322 at the UAM309005 at 8000 ft, Continue until the UAM314007 then turn left heading 241 degrees on downwind leg at 8000 ft. Maintain heading altitude until the UNZ357009 then start descent to the Initial Approach Fix, UNZ335009 at 6289 ft. Turn left onto the base leg heading 145 descending to the UNZ341006 at 5114 ft. Turn left on to final heading 062 degrees to the Final Approach Fix, the UNZ015008 at 3076 ft, continue approach to landing.

## Slide 4
UAM 276/007
8000
UAM 291/009
8000
UAM 310/007
8000
UAM 351/007
8000
IAF
UAM 011/009
6308
UAM 018/008
5697
UAM 028/007
5055
UAM 005/005
3562
FAF
UAM 354/004
3084
Missed Approach (C4) NW Field – RWY 24L: Commence missed approach at the UAM282006 .At 8000 ft, heading 048 degrees. Turn right heading 332 at the UAM276007 at 8000 ft, Continue until the UAM291009 then turn right heading 062 degrees on downwind leg at 8000 ft. Maintain heading altitude until the UAM351007 then start descent to the Initial Approach Fix, UAM011009 at 6308 ft. Turn right onto the base leg heading 150 descending to the UAM028007 at 5055 ft. Turn right on to final heading 242 degrees to the Final Approach Fix, the UAM354004 at 3084 ft, continue approach to landing.